## Slide 1: IOT based smart garage door opener Group- 4

## Slide 2: Deciding and ordering hardware components
Presenter- Gopikrishnan KG

## Slide 3: Contents
Microcontrollers used in the project
Components connected directly to Beaglebone Black
Components connected directly to Arduino Uno
Miscellaneous

## Slide 4: Block Diagram

## Slide 5: Microcontrollers used in the project
Beaglebone Black
Arduino Uno

## Slide 6: Beaglebone black
Main Micro controller in the project
Inputs to the MCU- IR Sensors, Arduino Uno, Limits Switch, and Push button
Outputs from the MCU- Buzzer, Relay Module, and Logic level controller.
All the components connected directly or indirectly to the MCU

## Slide 7: Slots, indicators, buttons and pins in beaglebone black board
P1- for power supply to the beaglebone black board
P3- for USB connection
P10- SD card slot (for ex booting)
P5- for internet access
P6- for HDMI access (TVs ,LCD screens etc)
P8- for UART,SPI,ADC,PWM,I2C communication
S3- Boot key
S2- Power key
S1- Reset key
4 user custom indicators
1 LED power indicator

## Slide 8: Main Features of beaglebone black

## Slide 9: General specifications
Operating Voltage : 5 V
Operating Current : 0.35 A
Operating Temperature : 0-70 degrees
Operating Humidity: 20%- 90%

## Slide 10: On board interfaces
1 10/100 M ethernet
1 LCD interface(24-bit, extended by P8 interface)
1 HDMI D type interface
1 high- speed USB 2.0 OTG interface with PHY
1 high-speed USB 2.0 HOST interface with PHY
1 Micro SD card slot
1 3-line debugging serial interface
1 interface for LCD, UART, eMMC ,I2C,SPI AND PWM
1 JTAG interface

## Slide 11: Component ordered from
Digikey Electronics
Part Number- BBB01-SC-505-ND
BEAGLEBONE BLK REV C AM3358BZCZ
https://www.digikey.ca/en/products/detail/BBB01-SC-505/BBB01-SC-505-ND/6210999?itemSeq=354364471

## Slide 12: Component order Status
Delivered

## Slide 13: Arduino uno
Directly connected to Beaglebone Black, the main MCU
Act as slave MCU
Used as a part of the system for alternative garage door access
Connected to Keypad and LCD display
Sends notification to the user via GSM module

## Slide 14: Slots, indicators, buttons, and pins
Digital I/O pins- 12
Analog input pins-6
Serial input pins-1
Serial output pins-1
Digital ground pins-1
Analog reference pin-1
USB plug in- 1
External power supply- 5V
5 V power pin- 1
3.3 V power pin-1

## Slide 15: General specifications
Processor: ATmega328P
Operating Voltage- 5V
Current- 50 mA max
Input voltage- 7-12V
DC current per I/O pin- 20ma
DC current for 3.3V pin-50 ma
Flash Memory- 32 KB
SRAM- 2KB
Clock Speed- 16 MHZ

## Slide 16: Component ordered from
Digikey Electronics, ARDUINO UNO R3 ATMEGA328P EVAL
Part Number- 1050-1024-ND
https://www.digikey.ca/en/products/detail/arduino/A000066/2784006?s=N4IgTCBcDaIIwAYCsCC0iwBZUDkAiIAugL5A
ORDER STATUS- DELIVERED

## Slide 17: Components connected Directly to Beaglebone black
L298N Motor driver controller
IR Proximity sensor
Push Button
Buzzer
Micro Switches
Power supply Adapter
Logic Level controller

## Slide 18: L298N Motor Driver Controller
Connected to the output pin of main MCU
Deals with controlling the operation of DC Motor
Has the ability to rotate the motor in either directions enabling the opening and closing of garage door
Performs the role of amplification of electric current, sufficient enough to drive the motor

## Slide 19: Connections in L298N dc motor driver

## Slide 20: specifications
Driver Model: L298N 2A.
Driver Chip: Double H Bridge L298N.
Motor Supply Voltage (Maximum): 46V.
Motor Supply Current (Maximum): 2A.
Logic Voltage: 5V.
Driver Voltage: 5-35V.
Driver Current:2A.
Logical Current:0-36mA.
Maximum Power (W): 25W.

## Slide 21: Component ordered from
Amazon,
PChero 2Packs L298N Motor Drive Controller Board Module, Dual H Bridge
Part Number- ISO17
https://www.amazon.ca/dp/B07C4B3DL4/ref=cm_sw_r_wa_apa_i_4E62PGXXSWMMZ6EYZNCE?psc=1

## Slide 22: Component Order status
Delivered

## Slide 23: IR PROXIMITY SENSOR
Comes into action when closing the garage door
Emits electromagnetic radiations to sense obstacles
Looks for change in field or return signal
Once obstacle detected, Communicates with Beaglebone Black which inturn activates Buzzer unit

## Slide 24: Specifications
Detection distance: 2-30 CMs
Detection angle: 35 degree
Can be used with 3-5V power modules
When turned on- Red power indicator light
Ability to drive a 5V relay

## Slide 25: Component ordered from
Amazon,
Gikfun IR sensor Obstacles Avoidance module, Case of 5pcs
Part Number :EK 1254
https://www.amazon.ca/dp/B07FFM7DYQ/ref=cm_sw_r_wa_apa_i_0MFESTK9QPSRGT214K7N

## Slide 26: Component order status
Delivered

## Slide 27: Push Button
Added as a part of security feature
Can come into action while opening and closing the door
Used to acknowledge the Buzzor

## Slide 28: Specifications
Made of Stainless steel
Mount Type- Snap-in Mount
Waterproof, Rust Proof
Dimesnion: 12mm
Current Rating: 2A
Operating Voltage- 12 -24 V

## Slide 29: Component Ordered from
Amazon, Gebildet 10 Pcs Waterproof Push Button Momentary Stainless Steel Push Button On Off 12mm 2A 12V/24V/125V/250V(High Head)
https://www.amazon.ca/Gebildet-Waterproof-Button-Momentary-Stainless/dp/B08671VD54/ref=sr_1_2?dchild=1&keywords=push+button&qid=1613076018&sr=8-2

## Slide 30: COMPONENT ORDER STATUS
Delivered

## Slide 31: BUZZER
Added as a security feature
Can come into action while opening and closing the door
Opening: Will notify the user when the door remains open more than set time
Closing: Will notify the user if any obstacle comes in between

## Slide 32: Specifications
Stable operation
Current: <25ma
Operating voltage: 5-8V DC
Optimal Voltage- 5 V

## Slide 33: Component ordered from
Amazon,
Cylewet 5v active buzzer , pack of 10pcs
Part Number: CLT1036
https://www.amazon.ca/dp/B07DDK92F5/ref=cm_sw_r_wa_apa_i_988HAS3XMSSDS9VYRQG9

## Slide 34: COMPONENT ORDER STATUS
Delivered

## Slide 35: Micro switches
Comes into action while opening and closing the door
Operated by the motion of a machine part or the presence of an object
Connected to garage door directly
Will detect the opening and closing of the door

## Slide 36: Specifications
Adopt Standard 22AWG wire
Current: 2A
Voltage: 300V
Convenient to plugin and use
Red line: Connect Vcc supply
Black line: to Ground
Green line: to Signal

## Slide 37: Component ordered from
Amazon,
PChero 5pcs Microswitches Mechanical En
dstop Switches with 70cm Cable RAMPS 1.4 for 3D Printer RepRap Prusa Mendel Makerbot Arduino Mega 2560 CNC
Part Number- iS008
https://www.amazon.ca/dp/B071JV158X/ref=cm_sw_r_wa_apa_i_T4SVA1ZN2XH2E1WKM99N

## Slide 38: COMPONENT ORDER STATUS
Delivered

## Slide 39: Power adapter
Voltage input- 90-264 VAC
Voltage Output- 5V
Current Output- 2A Max
Operating Temperature- 0-40 degrees
NL power consumption- 100mW max
Power- 10W

## Slide 40: Component ORDER STATUS
Delivered

## Slide 41: Logic Level controller
To change the voltage level
Interfaced with Arduino Uno and Wifi Module to change the voltage level received in the Beaglebone black.
Can convert from 3.3V to 5V and 5V to 3.3V

## Slide 42: VOLTAGE CONVERSION

## Slide 43: Component Ordered from
Digikey Electronics,
AC/DC WALL MOUNT ADAPTER 5V 10W
Part Number- 237-1385-ND
https://www.digikey.ca/en/products/detail/triad-magnetics/WSU050-2000/3094911?s=N4IgTCBcDa4MwHYC0BGOAOArEgcgERAF0BfIA

## Slide 44: Component order status
Delivered

## Slide 45: COMPONENTS CONNECTED DIRECTLY TO ARDUINO UNO
4*4 Keypad Matrix
20*4 LCD Display
GSM Module

## Slide 46: keypad matrix
Can play a role while opening and closing the garage door
Used as an alternate for garage door access in case of internet failure
Used for entering the password for garage door opening
Works along side with LCD display
Once opened, Closing of the garage door will be enabled by pressing a keypad key.

## Slide 47: Specifications
4*4 design
Voltage Rating- 35V DC max
Current rating- 100 mA
4 Numeric Keys, 4 English keys, 2 function keys
16 inputs
Used popularly for password security system

## Slide 48: How connections are done ?
There is a switch connecting each row and column, in total 16 inputs
Initially all switches are open, When user press either one switch it gets closed
Now there is a connection between that row and column
To connect to microcontroller, Connect the four pins to the columns as microcontroller input. The other four pins to the rows are connected as microcontroller outputs.
Inputs to the microcontroller is to be connected via a pull up resistor

## Slide 49: Which pin associate to which row and column ?
A Digital Multimeter will ease the job
Turn DMM to connectivity mode
Put the meter probe to first pin and the second one to the fifth pin
Press the buttons and observe which button gives beep sound.
Similarly continue with other pins, the connections of the keypad can be found

## Slide 50: COMPONENT ORDERED FROM
Amazon,
DIYmalls 4x4 Matrix Membrane Keypad 16 Keys Keyboard Module Array Switch for Arduino UNO R3
Part Number: B086ZGKDK9
https://www.amazon.ca/dp/B086ZGKDK9/ref=cm_sw_r_wa_apa_i_79TG40BP7MPFDC5C7MCA?_encoding=UTF8&psc=1

## Slide 51: COMPONENT ORDER STATUS
Delivered

## Slide 52: LCD DISPLAY
Can display 20 characters in a row, In total 80 characters
Can play a role while opening the garage door
Display the user inputs as a special character
Displays messages to the user

## Slide 53: Specifications
20*4 : 20 Columns,4 Rows
Contains IIC/I2C/TWI Serial Interface Adapter
Less I/O ports are occupied, only four - VCC, GND, SDA (serial data line), SCL (serial clock line).
Working Volage: 5V

## Slide 54: Component ordered from
Amazon,
WayinTop 20x4 2004 LCD Display Module with IIC/I2C/TWI Serial Interface Adapter for Arduino for Mega 2560 (Yellow Green/2004)
Part Number- WYTP22004YG
https://www.amazon.ca/dp/B07TXBV8MS/ref=cm_sw_r_wa_apa_i_40E5B0C5NGJZXYPYCCMW?psc=1

## Slide 55: COMPONENT ORDER STATUS
Delivered

## Slide 56: GSM Module
Plays a part while opening and closing the garage door
An important security feature
Notifies the user via SMS while the garage door is opened or closed
The user can be thus sure about the status of the garage door

## Slide 57: Specifications
SIM 800L Module
Based on GPRS standard
Operating voltage: 5V
Compact: suitable for embedded system designs
Self projectile card slot
Can conveniently change mobile-phone card
Use IPX interface
Can arbitrarily change the antenna
Stable operation

## Slide 58: Component ordered from
Amazon,
GSM Module
Part Number: YWBL-WHxiugqvk870
https://www.amazon.ca/dp/B07WZTXBSX/ref=cm_sw_r_wa_apa_i_3E9ADJAP9J1WT8PAS84Y

## Slide 59: COMPONENT ORDER status
Delivered

## Slide 60: Miscellaneous
DC 6V gear motor
Wifi Module
SD card
Silicone Hookup wires
LED Light assorted kit
PCB Board
Resistors
Beginners-kit

## Slide 61: DC gear mOTOR
To open and close the garage door
Operating Voltage- 6V
Models: 30/60/100/150/200/300/400/500RPM
No Load current : 200 mA
Stall current: 3 A (at 6V)
Choice: 150 RPM
3*55MM Lead Screw Thread Output Shaft

## Slide 62: CoMPONENT ORDER STATUS
Yet to be delivered

## Slide 63: Wifi module
ESP32
Small and Cheap package
Beaglebone black doesn’t have an inbuilt Wifi
To access Wifi services

## Slide 64: COMPONENT ORDER STATUS and link
Yet to be delivered
https://elmwoodelectronics.ca/9151182/orders/6551540dd659ed0a3c172ccfbdc9baff

## Slide 65: Memory Card
Make: SanDisk
Compact Flash Memory card format
Capacity: 16GB
May need a memory card reader
50 MBs read speed
Used for flashing Debian images

## Slide 66: Component order status
Delivered

## Slide 67: Silicone hookup wires
22 AWG Silicone hookup wires
22 Gauge Stranded tinned copper wire
Silicone insulation
Can withstand up to 200 degrees
Can operate with even 600 Volts
6 colors: Black, Red, Yellow, Green, Blue, White
Used to connect Sensor, Buzzer, and other components to the main unit

## Slide 68: Component order status
Yet to be delivered

## Slide 69: LED Light assorted kit
Size: 5mm
Colors: White, Yellow, Red , Green, and Blue.
Nominal Current : 20 mA
Maximum Current: 30 mA
Typical Voltage drop: 3.3 V
Maximum reverse voltage: 5V
To notify open/close status of the door

## Slide 70: COMPONENT ORDER STATUS
Delivered

## Slide 71: PCB Board
Color: Brown
Material: Epoxy glass fiber FR4
Size:3.94"x8.66",3.54"x5.9",2.76"x3.54",1.97"x2.76“
Used to solder components together

## Slide 72: COMPONENT ORDER STATUS
Delivered

## Slide 73: Resistor KIT
4 frequently used values 100 ohm,220 ohm,1k ohm, 10k ohm
Limit the flow of current through the circuit or divide voltages
Integral part to ensure operation without burning out

## Slide 74: Resistor VALUES AND THEIR TOLERANCES included in the KIT
Resistors from 0 ohm to 1 mega ohm and their tolerance level

## Slide 75: COMPONENT ORDER STATUS
Amazon,
LUTER 850pcs 30 Values Resistor Kit 1% 0 Ohm-1M Ohm 1/4W Metal Film
Resistors Assortment with a Plastic Box for DIY, Experiment
https://www.amazon.ca/dp/B0872Y9RXH/ref=cm_sw_r_wa_apip_9BQ5zzuVO7xdM
Delivered

## Slide 76: Beginners KIT
Contains capacitors, diodes and other essential components which we may need in the project

## Slide 77: COMPONENT ORDER STATUS
Amazon,
SparkFun Beginner Parts Kit
https://www.amazon.ca/dp/B01N1WJ3Z1/ref=cm_sw_r_wa_apip_S77JfKjKkdRjA
Delivered

## Slide 78: References
Retrieved from components101.com,(2020, April 13), L298N Motor driver module. URL: https://components101.com/modules/l293n-motor-driver-module#:~:text=L298%20Module%20Features%20%26%20Specifications%3A%201%20Driver%20Model%3A,25W.%2010%20Current%20Sense%20for%20each%20motor.%20
Retrieved from adafruit.com, Beaglebone black Data sheet. URL:https://cdn-shop.adafruit.com/datasheets/BBB_SRM.pdf
Retrieved from arduino.cc, Arduino UNO & Genuino UNO, URL: https://www.arduino.cc/en/Main/arduinoBoardUno&gt;
Retrieved from diymalls.com, 4*4 Matrix Keypad 16Keys Keyboard Module Array Switch for Arduino Microcontroller, URL: http://www.diymalls.com/16-Keys-Matrix-Keypad-4X4-Keyboard
Retrieved from bhphotovideo.com, SanDisk 16GB Ultra CompactFlash Memory Card, URL: https://www.bhphotovideo.com/c/product/1012243-REG/sandisk_sdcfhs_016g_a46_16gb_ultra_compactflash_memory.html

## Slide 79: References
Retrieved from plusivo.com, PLUSIVO 22AWG HOOKUP WIRE KIT, URL: https://www.plusivo.com/home/67-plusivo-22awg-hook-up-wire-kit-600v-tinned-stranded-silicone-wire-of-6-different-colors-x-23-ft-each.html
Retrieved from URL: https://sites.google.com/site/markgurries/home/part-sources/led-s/led-electrcial-ratings
Retrieved from electricalfundablog.com, Infrared Sensor- How it works, Types , Applications, Advantage & Disadvanatge, URL: https://electricalfundablog.com/infrared-sensor/
Retrieved from gadgetronics.com, Logic level controller circuit- 5v to 3.3v and vice versa, URL:https://www.gadgetronicx.com/logic-level-converter-5v-3-3v/
Retrieved from industrialshields.com, WiFi /Bluetooth Module ESP32. URL:https://www.industrialshields.com/blog/arduino-industrial-1/post/wifi-bluetooth-module-esp32-133

## Slide 80: THANKS TO
Professor MIKE ALESHAMS , my GROUP MATES and EVERYONE for listening